## Slide 1: title

## Slide 2: Slide 1 — Title & Goals
Title: Handover in LEO NTN: A4/A5/D2, Traditional vs AI-enhanced
Goals:
Summarize 3GPP A4/A5/D2 measurement events for HO triggers
Compare Measurement Report (MR)-based and Non-MR-based HO (traditional & AI)
Map to LEO NTN specifics: moving beams, ephemeris, long RTT, Doppler

## Slide 3: Slide 2 — References Used (Selected)
3GPP TS 38.331 RRC (Rel-18+): Events A4, A5, D2; SIB19 movingReferenceLocation
3GPP NTN overview: https://www.3gpp.org/technologies/ntn-overview
ETSI TR 21.918 (Rel-18): NTN mobility and measurement updates
MDPI (2023): ML-Based HO in NTN — https://www.mdpi.com/2079-9292/12/8/1759
arXiv (2025): Handover Delay Minimization in NTN — https://arxiv.org/abs/2501.17331

## Slide 4: Slide 3 — Outline (5 Topics)
A4: trigger & params
A5: Th1/Th2 logic
D2: moving refs (SIB19)
CHO/L3 filter/offsets
Pipeline

## Slide 5: Slide 4 — Topic 1 Outline: 3GPP Measurement Events
A4: Neighbor better than threshold (RSRP/RSRQ/RS-SINR)
A5: Serving below Th1 & neighbor above Th2
D2: Distance-based using moving references (LEO/ephemeris)
Parameters: Hys, thresholds, TTT, Ofn/Ocn
NTN hooks: SIB19 ephemeris, CHO, moving beams
Event | Enter condition (summary) | Leave condition (summary) | Primary inputs | Typical LEO use
A4 | Neighbor metric above threshold (with offsets, minus Hys) | Neighbor metric falls below threshold (plus Hys) | RSRP/RSRQ/SINR, Ofn, Ocn, Hys | Quick neighbor upgrade; intra-frequency, overlapping beams
A5 | Serving below Th1 AND neighbor above Th2 | Serving recovers OR neighbor falls below Th2 | Mp, Mn, Hys, Th1, Th2, Ofn, Ocn | Stable inter-beam/inter-sat HO
D2 | UE far from serving moving ref AND close to candidate moving ref | Serving distance falls OR candidate distance grows | Ml1, Ml2, HysLocation, Th1, Th2, ephemeris | Predictive HO aligned with beam motion

## Slide 6: Slide 5 — Event A4 (Neighbor > Threshold)
Concept: Trigger when neighbor’s metric exceeds configured threshold
Variables: Mn, Ofn, Ocn, Hys, Thresh
Enter: Mn + Ofn + Ocn − Hys > Thresh
Leave: Mn + Ofn + Ocn + Hys < Thresh
Notes: Works for CondEvent A4; candidate PSCell/SCG in CHO
Symbol | Definition | Unit | LEO NTN Tip
Mn | Neighbor cell/beam measurement | dBm (RSRP) / dB (RSRQ,SINR) | Use per-beam filtered RSRP with longer window
Ofn | Measurement object (frequency) offset | dB | Correct inter-frequency bias
Ocn | Cell/beam-specific offset | dB | Balance asymmetric beam footprints
Hys | Event hysteresis | dB | Increase to avoid edge ping-pong (2–4 dB)
Thresh | A4 threshold | same as Mn | Start near edge budget − margin

## Slide 7: Slide 6 — Event A5 (Serving < Th1, Neighbor > Th2)
Enter: (Mp + Hys < Th1) AND (Mn + Ofn + Ocn − Hys > Th2)
Leave: (Mp − Hys > Th1) OR (Mn + Ofn + Ocn + Hys < Th2)
Use: Inter-beam/inter-satellite HO; fewer false triggers vs A4
Tune: Hys, Th1, Th2, TTT
Engineering trade-offs:
Scenario | Th1 (dBm) | Th2 (dBm) | Hys (dB) | TTT (ms) | Rationale
Moderate speed, medium RTT | −97 | −95 | 3 | 160 | Stability vs latency balance
High speed, long RTT | −95 | −94 | 4 | 240 | Earlier trigger on serving drop
Dense beams | −98 | −96 | 2 | 120 | Reduce ping-pong with lower Hys

## Slide 8: Slide 7A — Event D2 (Distance-Based, NTN)
Distance to moving reference locations using SIB19 ephemeris + epoch
Enter: (Ml1 − Hys > Th1) AND (Ml2 + Hys < Th2)
Leave: (Ml1 + Hys < Th1) OR (Ml2 − Hys > Th2)
Benefits: Predictive HO aligned with beam geometry; less noisy than RSRP
Inputs & mapping to TS 38.331/SIB19:

## Slide 9: Slide 7B — Event D2 Inputs & Pseudo-code
Inputs & mapping to TS 38.331/SIB19:
Pseudo-code:
Parameter impacts on KPIs:
Suggested starting grid (LEO trials): Hys ∈ {2,3,4} dB; TTT ∈ {120,160,240} ms; Th1/Th2 by link budget − margins
Pseudo-code:
Element | Source | Purpose
movingReferenceLocation | SIB19 (serving cell) | Defines serving moving reference for Ml1
referenceLocation | MeasObjectNR | Defines candidate moving reference for Ml2
epoch time & ephemeris | SIB19/MeasObjectNR | Propagate satellite positions
UE position/time | UE GNSS / network | Compute distances to moving references
hysteresisLocation | reportConfigNR | Hys for D2 event
distanceThreshFromReference1/2 | reportConfigNR | Th1/Th2 for D2

## Slide 10: Slide 7C — Event D2 Example & Notes
Numeric example:
Th1 = 100 km, Th2 = 60 km, Hys = 5 km; Ml1 = 120 km, Ml2 = 50 km
120 − 5 > 100 ✓ and 50 + 5 < 60 ✓ → D2 ENTERS (pre-emptive HO viable)
Notes:
Use UE position covariance to inflate Hys if GNSS error is large
KPI | Definition | Typical Target | Notes
HOP | #HOs / time or distance | Context-dependent | Too high → instability
HOF | Failed HOs / total HOs | < 2–5% | Includes T310 expiry, RA fail
Ping-pong | HO back within τ | < 5–10% | τ e.g., 30–60 s
HOD | Time from trigger→RQ | As low as possible | Reduce with CHO/CFRA
Throughput | DL/UL average | Maximize | Avoid HO during bursts

## Slide 11: Slide 8A — NTN Adaptations for Events
Long RTT → increase TTT; conservative Hys
Moving beams → combine D2 with A4/A5; CHO usage
Technique selection:
Offsets (Ofn/Ocn) per-beam calibration
L3 filtering windows extended; GNSS/timing uncertainty considered
Approach | Data needs | Pros | Cons | Where to use
Heuristic (A4/A5 tuning) | Low | Simple, explainable | Limited adaptivity | Baseline, safety fallback
Supervised ML | Moderate (labeled) | Data-efficient, fast infer | Labeling cost, drift | Dynamic thresholds/target select
RL (SAC/DQN/PPO) | High (sim logs) | Learns timing & strategy | Training complexity | High dynamics, long-horizon control

## Slide 12: Slide 8B — NTN Techniques & Feature Set
Technique selection:
Feature dictionary (examples):
Filtering tips:
Increase L3 filter window; avoid over-smoothing near beam edges
Use per-beam Ofn/Ocn to correct persistent bias
Approach | Data needs | Pros | Cons | Where to use
Heuristic (A4/A5 tuning) | Low | Simple, explainable | Limited adaptivity | Baseline, safety fallback
Supervised ML | Moderate (labeled) | Data-efficient, fast infer | Labeling cost, drift | Dynamic thresholds/target select
RL (SAC/DQN/PPO) | High (sim logs) | Learns timing & strategy | Training complexity | High dynamics, long-horizon control

## Slide 13: Slide 9 — Topic 2 Outline: MR-based HO (Traditional)
A4 vs A5 HO count & ping-pong (illustrative):
Note: Values illustrative; tune per network
HO pipeline: measure→report→decide→execute
Event selection: A4 vs A5
Types: inter-beam, inter-sat, inter-frequency
Policy | HOs/UE/hour | Ping-pong % | HOF %
A4-only | 14.2 | 12.5 | 4.1
A5 (tuned) | 9.8 | 5.3 | 3.2
A5 + D2 + CHO | 8.5 | 3.8 | 2.6

## Slide 14: Slide 10A — MR-based HO Pipeline
UE measures: RSRP/RSRQ/SINR per beam/cell
Config: A4/A5 with Hys, TTT, Ofn/Ocn
Reports: periodic/aperiodic; reportQuantity
Decision: neighbor ranking; CHO list
Execute: RRC Reconf; RA; path switch

## Slide 15: Slide 10B — MR-based HO Reporting & Timeline
Reporting fields (selected):
Execution timeline (NTN):
Reporting fields (selected):
Practical:
Maintain CHO list to avoid decision-time delays
Item | Example values | Purpose
reportQuantity | rsrp, rsrq, sinr | What metrics to include
triggerType | event, periodic | Event-based (A4/A5/D2) vs periodic
reportAddNeighMeas | true/false | Include neighbor details in report
maxReportCells | e.g., 4–8 | Limit payload size
ttt | 80–320 ms | Debounce spurious triggers

## Slide 16: Slide 11 — A4 vs A5 in NTN
A4 pros: simple, fast; cons: ping-pong at edges
A5 pros: stable dual-condition; cons: may trigger late
Practice: A5 for inter-beam; A4 for dense co-beams

## Slide 17: Slide 12 — Parameter Tuning (Traditional)
Hys: 2–4 dB for LEO
TTT: 80–320 ms (RTT-aware)
Ofn/Ocn: per-frequency/beam bias
L3 filtering: a=0.5–0.9; extended windows
Load-aware Th2 adjustment

## Slide 18: Slide 13 — Execution Options in NTN
CHO: pre-configured candidates + conditions (A4/A5/D2)
DAPS/make-before-break when feasible
RA: CFRA with beam sweep; enlarged RA window
Timing: large TA + Doppler compensation; UL BWP preset
Core: efficient path switch to reduce HOD

## Slide 19: Slide 14 — KPIs and Trade-offs
Supervised ML configuration example:
KPIs: HOP, HOF, Ping-pong rate, throughput, latency
Trade-offs: TTT vs ping-pong; Hys vs late HO; CHO size vs overhead
Component | Choice
Model | XGBoost (depth 6, 200 trees)
Labels | Best target/no-HO from oracle planner
Features | Slide 15/16 dictionary
Output | ΔTh1, ΔTh2, target rank
Inference budget | < 2 ms per UE per eval
Update | Nightly with drift check

## Slide 20: Slide 15 — Topic 3 Outline: MR-based HO (AI-Enhanced)
Supervised learning, RL
Feature set: MR stats, velocity, Doppler, beam IDs, history
Reward: HOF−, ping-pong−, throughput+, dwell-time+
RL configuration example (SAC):
Deployment: online/offline, safety guards, fallback
Element | Setting
State | [RSRP vector, trends, speed, elevation, TimeToEdge_pred]
Action | {HO-now, wait, target-id, ΔTTT, ΔHys}
Reward | +throughput +dwell −HOF −ping-pong −delay
Training | Offline on digital twin logs + domain randomization
Safety | Action clipping; A5/CHO fallback; max HO rate

## Slide 21: Slide 16 — Supervised ML for MR-based HO
Labels: optimal target/HO/no-HO from oracle or simulation
Models: XGBoost/LightGBM, shallow NN
Pros: data-efficient; interpretable
Cons: distribution shift; retraining cadence
With A5: learn context-aware Th1/Th2 adjustments

## Slide 22: Slide 17 — RL for MR-based HO
State: MR vectors, neighbor ranks, speed, elevation
Action: HO now / wait / target; adjust TTT/Hys
Reward: +throughput, +dwell, −HOF, −ping-pong, −delay
Algorithms: SAC, DQN, PPO; safe RL
Non-AI schedule table (example):
Rule | Condition | Action
Beam-edge | TimeToEdge_pred < Δt_edge | Pre-emptive HO to best neighbor
Elevation | Elevation_target − Elevation_serving > Δelev | Candidate add to CHO
Link budget | RSRP_pred_target − RSRP_pred_serving > δ | Lower Th2 by δ_margin
GEO fallback | Ephemeris stale > T_max | Switch to MR-based policy

## Slide 23: Slide 18 — AI Pipeline & Safeguards
Offline training with digital twins; domain randomization
Online: shadow mode; guarded activation
Guardrails: min TTT, max HO rate, SINR floor; CHO fallback
Drift detection; rollback triggers; XAI for ops

## Slide 24: Slide 19 — Topic 4 Outline: Non-MR-based HO (Traditional)
Location/ephemeris triggers (D2)
Scheduled HO on beam footprints
Kinematic trajectory prediction (non-AI)
RRC support: SIB19, movingReferenceLocation/referenceLocation
Fallback to MR when position uncertainty high

## Slide 25: Slide 20 — D2-based HO in Practice
Inputs: UE GNSS, SIB19 ephemeris, beam geometry
Configure: Th1/Th2, HysLocation, TTT; CHO candidates
Execution: pre-emptive HO before beam-edge crossing
Benefit: lower HOF under rapid beam motion

## Slide 26: Slide 21 — Scheduled/Rule-based Non-MR HO
Beam schedule: HO at footprint boundaries
Elevation rule: target elevation > serving elevation + Δ
Link budget rule: predicted RSRP_target − serving > margin
Pros: predictable, low overhead; Cons: error sensitivity

## Slide 27: Slide 22 — Topic 5 Outline: Non-MR-based HO (AI-Enhanced)
Mixed policy (A5 + D2 + CHO) — detailed logic:
Trajectory prediction: LSTM/Kalman/Particle filter
Graph RL / Multi-agent RL over constellation-beam graph
Contextual bandits for target selection
Uncertainty-aware decisions with covariance
Step | Condition | Action
1 | D2 Enter within Δt_pre | Arm CHO for target(s)
2 | A5 Enter | Execute HO if CHO armed else arm & execute
3 | D2 Leave imminent | Defer HO unless Mp below outage margin
4 | Load high | Add +β to Th2; skip if target overloaded
5 | Guard | Enforce min dwell τ, cap HO rate

## Slide 28: Slide 23 — AI for Non-MR HO
Trajectory & dwell prediction: LSTM + kinematic, particle filter
Decision: contextual bandit; multi-agent RL coordinates inter-sat HO
Safety: fallback to A5/CHO if uncertainty > threshold

## Slide 29: Slide 24 — Tables: Event-to-Use-Case Mapping
Risks & mitigations table:
Event | Metric | Best for | Notes
A4 | RSRP/RSRQ/SINR | Simple neighbor upgrade | Fast; can ping-pong on edges
A5 | Serving↓ & Neighbor↑ | Stable inter-beam HO | Reduced false triggers vs A4
D2 | Distance to moving refs | Predictive LEO HO | Needs SIB19, GNSS, geometry

## Slide 30: Slide 25 — Tables: Parameter Heuristics (Start Points)
Parameter | Terrestrial | LEO NTN Suggestion
Hys (dB) | 1–2 | 2–4
TTT (ms) | 40–160 | 80–320
Ofn/Ocn | Small | Per-beam/freq calibration
HysLocation | N/A | Tune vs position error σ

## Slide 31: Slide 26 — Design Checklists
Pre-trial: validate SIB19 ephemeris; UE GNSS accuracy budget
Config: A5 + D2 + CHO; enable logging (MR, pos, ephemeris, HO)
Trials: sweep Hys/TTT; monitor HOF/ping-pong
Post: fit ML baselines; run shadow mode

## Slide 32: Slide 27 — Example Mixed Policy (A5 + D2 + CHO)
If D2 Enter within Δt → pre-emptive HO via CHO
Else if A5 Enter → execute; defer if D2 Leave imminent
Guards: min dwell τ; cap HO rate/UE; load-aware +β dB to Th2

## Slide 33: Slide 28 — Risks & Mitigations
Ephemeris/position errors → HysLocation + uncertainty margins
Beam steering changes → faster CHO refresh cadence
RA/TA issues → CFRA, extended RA windows
Model drift → continuous eval and rollback plan

## Slide 34: Slide 29 — Implementation Notes (Standards)
TS 38.331:
A4/A5: thresholds, hysteresis, TTT, offsets
D2: distance thresholds, hysteresisLocation; SIB19 hooks
CHO: conditional events & candidate cells
Reporting: reportQuantity, reportAddNeighMeas, L3 filtering

## Slide 35: Slide 30 — Key Takeaways
A5 default for inter-beam; complement with D2 for predictiveness
Tune Hys/TTT for LEO; calibrate offsets per beam
CHO reduces HOF in moving-beam scenarios
AI learns context-aware thresholds/timing with guardrails

## Slide 36: Slide 31 — Further Reading
TS 38.331: https://www.etsi.org/deliver/etsi_ts/138300_138399/138331
ETSI TR 21.918 (NTN): https://www.etsi.org/deliver/etsi_TR/121900_121999/121918
3GPP NTN overview: https://www.3gpp.org/technologies/ntn-overview
MDPI 2023: https://www.mdpi.com/2079-9292/12/8/1759
MDPI 2025: https://www.mdpi.com/2079-9292/14/8/1494

## Slide 37: Slide 32 — Appendix: Abbreviations
CHO: Conditional Handover; CFRA: Contention-Free Random Access
HOF: Handover Failure; HOD: HO Delay; HOP: HO Probability
SIB19: System Information Block with ephemeris/moving refs (NTN)
Ofn/Ocn: Offset (frequency/cell); Hys: Hysteresis; TTT: Time To Trigger