## Slide 1: Outline
3GPP Measurement Events for Handover Trigger
Measurement Report-based Handover (Traditional)
  RSS/RSRP-based、Elevation Angle、Service Time、Multi-Criteria (MADM)
Measurement Report-based Handover (AI-Enhanced)
  Deep Q-Network Based、Multi-Agent DQN、MORL、Game Theory + RL (Nash-SAC)
Non-Measurement Report-based Handover (Traditional)
  Location-based、Time-based、Conditional Handover、Graph-based Methods
Non-Measurement Report-based Handover (AI-Enhanced)
  Predictive Deep RL、GNN、Transformer-based Channel Prediction、Joint Optimization with MPC

## Slide 2: Introduction to LEO Satellite Networks
Key Characteristics:
Altitude: 500-2000 km
Orbital Speed: ~7.5 km/s
Coverage per Satellite: 2-4 minutes visibility
Global Coverage: Mega-constellations (1000+ satellites)
Major Challenges:
Frequent Handovers: Every 5-6 seconds
Dynamic Topology: Constantly changing network structure
Propagation Delays: 1-4 ms one-way
Doppler Effects: High frequency shifts
Small Signal Variations: Similar RSRP at cell center and edge

## Slide 3: ISL/Backhaul Constraints & Mobility
ISL changes alter routing, impact HO timing
Backhaul bottlenecks can negate RSRP gains
Joint HO + backhaul‑aware selection
Plan handovers around ISL reconfiguration
Refs: NTN architecture surveys (2024)

## Slide 4: 3GPP Measurement Events for Handover Trigger
Key Variables:
D2 Event: Ml1 = distance from serving satellite, Ml2 = distance from neighbor satellite
A4 Event: Mn = neighbor cell measurement (RSRP/RSRQ/RS-SINR)
A5 Event: Mp = serving cell measurement, Mn = neighbor cell measurement
LEO-Specific Advantages:
D2 Event: Uses satellite ephemeris data and UE position for precise distance calculation
A4 Performance: 30% better performance than A3 in LEO environments
A5 Dual Threshold: Prevents ping-pong effects in weak signal areas
Event | Description | Entering Condition | LEO Applicability
D2 | Distance-based trigger | Ml1 – Hys > Thresh1 AND Ml2 + Hys < Thresh2 | Optimal for NTN/LEO satellites
A4 | Neighbor better than threshold | Mn + Ofn + Ocn – Hys > Thresh | Good for LEO environments
A5 | Serving worse than Thresh1 AND neighbor better than Thresh2 | Mp + Hys < Thresh1 AND Mn + Ofn + Ocn – Hys > Thresh2 | Coverage hole scenarios

## Slide 5: A4/A5 Practical Tuning (3GPP TS 38.331)
A4 enter/leave: hysteresis (Hys) to suppress ping‑pong
A5 dual threshold: Mp < Thresh1 AND Mn > Thresh2
Offsets: Ofn (freq), Ocn (cell) steer preference
Use TTT + Hys + offsets; calibrate by Doppler/UE speed
Source: 3GPP TS 38.331 (Rel-18)

## Slide 6: Event D2 Mechanics (3GPP TS 38.331)
Moving references + ephemeris (SIB19)
Enter if: Ml1 – Hys > Thresh1 AND Ml2 + Hys < Thresh2
Leave if: Ml1 + Hys < Thresh1 OR Ml2 – Hys > Thresh2
Units: distances (meters); Hys/Thresh in same units
Source: 3GPP TS 38.331 (Rel-18)

## Slide 7: Measurement Report-based Handover (Traditional Approaches)
Standard Handover Procedure:
1. UE Measurements → Serving & neighbor satellites
2. Measurement Reports → Sent to serving gNB/satellite
3. Network Decision → Handover target selection
4. Handover Execution → Switch to target satellite
Measurement-Based Challenges in LEO:
- Doppler Shift: Rapid frequency changes affect measurements
- Measurement Delays: 150-300ms propagation delays
- Small Signal Difference: Similar RSRP between cell center and edge
Method | Description | Advantages | Disadvantages
RSS/RSRP-based | Select strongest signal | Simple, 3GPP standard | Frequent handovers, ping-pong
Elevation Angle | Highest elevation priority | Better link quality, lower path loss | May not optimize service time
Service Time | Maximize visibility duration | Reduces HO frequency, predictable | May sacrifice signal quality
Multi-Criteria (MADM) | Weighted combination using AHP/TOPSIS | Balanced approach, customizable | Static optimization, complexity

## Slide 8: Measurement Latency & Doppler Mitigation
Latency: 150–300 ms round trip → stale reports
Doppler: rapid frequency shifts bias RSRP/RSRQ
Mitigate: higher report rate, filtering, Doppler-compensation
Fallback: D2/CHO when measurements are unreliable
Refs: NTN surveys (2024), 3GPP NTN overview

## Slide 9: Measurement Report-based Handover (AI-Enhanced Approaches)
Deep Reinforcement Learning Methods:
Deep Q-Network (DQN) Based
State: [RSRP, elevation angle, visible time, load, interference]
Action: Target satellite selection from coverage set
Reward: Throughput - handover penalty - outage cost
Innovation: Learns optimal measurement thresholds dynamically
Performance: 30-50% reduction in handover rate
Multi-Agent Deep Q-Network (MADQN)
Architecture: Distributed learning, each UE as independent agent
Coordination: Implicit through environment interaction
State Space: Local information only (scalable)
Benefits: 95% handover reduction, real-time adaptation
Paper Reference: Lee et al. (2025) - simultaneous decision making

## Slide 10: Game‑Theoretic RL: Nash‑SAC
Models multi‑user interactions as a game
Computes Nash‑consistent policies with SAC
Improved stability under heavy load/mobility
Targets: drones/aircraft/ground terminals
Source: Nash‑SAC LEO HO (arXiv:2402.00091)

## Slide 11: Multi‑Agent RL & Stability
Distributed agents (UEs) with local observations
Coordination via environment; avoid oscillations
Load‑aware MARL (GLOBECOM 2020) improves balance
Design: reward shaping + entropy regularization
Refs: MARL for LEO HO (survey, proceedings)

## Slide 12: Protocol‑Learning DRL for Handover
End‑to‑end learning of HO rules from experience
State: channel stats, geometry, timers; Action: HO trigger
Reward: throughput − HO penalty − outage cost
Fewer outages vs fixed rules in simulations
Source: Handover Protocol Learning for LEO (arXiv:2310.20215)

## Slide 13: Measurement Report-based Handover (AI-Enhanced Approaches)
Multi-Objective Reinforcement Learning (MORL)
Objectives: Maximize [throughput, QoS] + Minimize [handovers, energy]
Method: Pareto-optimal solution selection
Algorithm: MODQN (Multi-Objective DQN)
Application: Multi-beam LEO satellites
Achievement: 62% throughput improvement
Game Theory + RL (Nash-SAC)
Approach: Nash equilibrium in multi-user scenarios
Users: Aircraft, drones, ground terminals
Algorithm: Soft Actor-Critic with Nash solutions
Performance: 16% handover reduction, 48% utility improvement
Advantage: Handles heterogeneous user requirements

## Slide 14: Non-Measurement Report-based Handover (Traditional)
Approaches Without Measurement Reports:
Location-based Handover
3GPP D2 Event: Uses UE position and satellite ephemeris from SIB19
Trigger Condition: Distance calculations based on GPS coordinates
Advantages: Zero measurement delays, predictable, eliminates RLF
Implementation: Real-time distance monitoring with hysteresis
Time-based Handover
Mechanism: Pre-scheduled switching using Two-Line Element (TLE) data
Method: Timer-based handover at predetermined orbital positions
Advantages: Completely deterministic, no measurement overhead
Limitation: Cannot adapt to dynamic channel conditions or interference

## Slide 15: Graph‑based Planning Details
Time‑expanded graph: nodes=satellite/beam/time
Edges weighted by link quality/HO cost
Solvers: shortest path, min‑cost flow
Complexity O(N^3 T); prune by visibility windows
Refs: NTN optimization literature

## Slide 16: Location‑based HO with Particle Filter
Fuses ephemeris + UE motion; robust to noise
Particle filter tracks geometry for trigger timing
Integrates with D2/CHO to reduce RLFs
Hybrid with RL for adaptive thresholds
Ref: Location‑based HO + PF (MDPI Electronics)

## Slide 17: Non-Measurement Report-based Handover (Traditional)
Approaches Without Measurement Reports:
Conditional Handover (CHO)
3GPP Rel-16: Enhanced mobility for Non-Terrestrial Networks (NTN)
Pre-configuration: Target satellite parameters configured in advance
Execution Triggers: Time-based, location-based, or hybrid conditions
Benefits: 84% reduction in signaling overhead, improved reliability
Graph-based Methods
Network Flow: Time-expanded graphs with satellites as nodes
Algorithms: Shortest path, minimum cost flow, maximum flow solutions
Optimization: Global handover path planning considering future states
Complexity: O(N³T) for N satellites and T time slots

## Slide 18: Non-Measurement Report-based Handover (AI-Enhanced)
AI-Enhanced Predictive Methods:
Predictive Deep RL
Orbital Prediction: Skip measurement reports using Keplerian orbital mechanics
Training Data: Historical satellite positions, channel conditions, user mobility
Neural Architecture: LSTM + DQN for temporal sequence learning
Benefits: 150-300ms latency reduction, proactive handover decisions
Graph Neural Networks (GNN)
Dynamic Topology: Learn optimal paths in time-varying satellite constellation
Node Features: Satellite position, load, beam coverage, interference level
Edge Weights: Inter-satellite distances, link quality, handover costs
Performance: Distributed decision making with global optimization

## Slide 19: CHO Trigger Prediction (XGBoost)
Supervised model predicts success of CHO
Features: geometry, timing, recent KPIs
Reduces failed HOs and signaling
Combines with D2 guardrails
Ref: Two‑Step XGBoost for CHO (2023)

## Slide 20: Transformer‑based Channel Prediction
Attention captures long‑range temporal deps
Inputs: RSRP history, Doppler, geometry
Horizon: 10–30 s for proactive HO
Feeds MPC or RL for look‑ahead
Refs: LEO channel prediction (Transformer)

## Slide 21: Non-Measurement Report-based Handover (AI-Enhanced)
Transformer-based Channel Prediction
Attention Mechanism: Learn long-term channel dependencies
Input Sequence: Historical RSRP, satellite positions, Doppler shifts
Prediction Horizon: 10-30 seconds ahead for proactive handover
Accuracy: 95% correlation with actual measurements
Joint Optimization with Model Predictive Control (MPC)
Multi-Objective: Handover decisions + resource allocation + power control
Prediction Model: Satellite constellation dynamics and user mobility
Optimization Horizon: 60-120 seconds rolling window
Results: 62% throughput improvement, 40% energy savings
Advanced AI Features:
Digital Twin Networks: Real-time network state mirroring
Federated Learning: Privacy-preserving distributed training
Meta-Learning: Fast adaptation to new satellite constellations

## Slide 22: Performance Comparison Analysis
Quantitative Performance Metrics:
Metric | Traditional Methods | AI-Enhanced Methods | Best Performing Approach
Handover Rate | 0.8-1.2 HO/min | 0.05-0.2 HO/min (85% ↓) | MADQN + Location-based
Radio Link Failures | 15-40% | <1% | CHO + Predictive RL
Average Throughput | 12-18 Mbps | 20-29 Mbps (62% ↑) | Joint Optimization MPC
End-to-End Latency | 180-320 ms | 90-160 ms (50% ↓) | Non-measurement + GNN
Signaling Overhead | 450-680 msgs/min | 70-120 msgs/min (84% ↓) | Distributed MARL
QoS Satisfaction Time | 65-80% | 92-98% | Nash-SAC multi-objective
Energy Efficiency | 2.1-2.8 bits/Joule | 3.4-4.2 bits/Joule (85% ↑) | Energy-aware DRL

## Slide 23: Implementation Guidelines
Default to D2 + CHO; enable A4/A5 with tuned Hys/TTT
Use offsets (Ofn/Ocn) to shape neighbor preference
Predict visibility/Doppler for proactive HO
Deploy RL incrementally with fallback/guardrails
Cite: 3GPP TS 38.331; CHO (Rel‑16); RL papers

## Slide 24: Evaluation Methodology
KPIs: HO rate, RLF, throughput, E2E latency, QoS%
Scenarios: urban, maritime, aerial (fast UEs)
Constellations: Walker/mega‑LEO layouts
Baselines: A4/A5/D2, CHO; vs RL/MPC/graphs
Refs: NTN/LEO surveys 2023–2024

## Slide 25: Performance Comparison Analysis
Performance vs. Complexity Trade-offs:
N = number of satellites, T = time horizon, M = state space size, K = number of users
Approach Category | Computational Complexity | Implementation Difficulty | Real-time Capability | Performance Gain
Traditional Rule-based | O(N) | Low | Excellent | Baseline
3GPP Events (D2, A4, A5) | O(N log N) | Medium | Very Good | 20-30%
Graph-based Optimization | O(N³T) | High | Poor | 35-45%
Single-agent RL (DQN) | O(MN) | Medium-High | Good | 50-65%
Multi-agent RL (MADQN) | O(KMN) | High | Very Good | 70-95%

## Slide 26: LEO Satellite Handover: Research-backed Practices
Baseline Triggers (3GPP NTN)
  D2: Distance-based using ephemeris + UE location
  A4/A5: Thresholds + hysteresis + time-to-trigger
Conditional Handover (Rel-16)
  Pre-configure targets; trigger on time/location/quality
  Cuts signaling; improves reliability in fast mobility
Learning-based Policies (LEO)
  Protocol-learning DRL: Learns HO rules end-to-end; fewer outages vs fixed rules
  Nash-SAC MARL: Stabilizes multi-user decisions under load
Practical Tips
  Use D2/CHO as fallback; prevent ping-pong via hysteresis/TTT
  Predict visibility/Doppler; refine with RL where feasible
Sources
  CHO (Rel-16): arXiv:2204.01283; Protocol-learning DRL: arXiv:2310.20215; Nash-SAC MARL: arXiv:2402.00091; 3GPP NTN overview