## Slide 1: Outline
3GPP Measurement Events for Handover Trigger
Measurement Report-based Handover (Traditional)
  RSS/RSRP-based、Elevation Angle、Service Time、Multi-Criteria (MADM)
Measurement Report-based Handover (AI-Enhanced)
  Deep Q-Network Based、Multi-Agent DQN、MORL、Game Theory + RL (Nash-SAC)
Non-Measurement Report-based Handover (Traditional)
  Location-based、Time-based、Conditional Handover、Graph-based Methods
Non-Measurement Report-based Handover (AI-Enhanced)
  Predictive Deep RL、GNN、Transformer-based Channel Prediction、Joint Optimization with MPC

## Slide 2: Introduction to LEO Satellite Networks
Key Characteristics:
Altitude: 500-2000 km
Orbital Speed: ~7.5 km/s
Coverage per Satellite: 2-4 minutes visibility
Global Coverage: Mega-constellations (1000+ satellites)
Major Challenges:
Frequent Handovers: Every 5-6 seconds
Dynamic Topology: Constantly changing network structure
Propagation Delays: 1-4 ms one-way
Doppler Effects: High frequency shifts
Small Signal Variations: Similar RSRP at cell center and edge

## Slide 3: 3GPP Measurement Events for Handover Trigger
Key Variables:
D2 Event: Ml1 = distance from serving satellite, Ml2 = distance from neighbor satellite
A4 Event: Mn = neighbor cell measurement (RSRP/RSRQ/RS-SINR)
A5 Event: Mp = serving cell measurement, Mn = neighbor cell measurement
LEO-Specific Advantages:
D2 Event: Uses satellite ephemeris data and UE position for precise distance calculation
A4 Performance: 30% better performance than A3 in LEO environments
A5 Dual Threshold: Prevents ping-pong effects in weak signal areas
Event | Description | Entering Condition | LEO Applicability
D2 | Distance-based trigger | Ml1 – Hys > Thresh1 AND Ml2 + Hys < Thresh2 | Optimal for NTN/LEO satellites
A4 | Neighbor better than threshold | Mn + Ofn + Ocn – Hys > Thresh | Good for LEO environments
A5 | Serving worse than Thresh1 AND neighbor better than Thresh2 | Mp + Hys < Thresh1 AND Mn + Ofn + Ocn – Hys > Thresh2 | Coverage hole scenarios

## Slide 4: Measurement Report-based Handover (Traditional Approaches)
Standard Handover Procedure:
1. UE Measurements → Serving & neighbor satellites
2. Measurement Reports → Sent to serving gNB/satellite
3. Network Decision → Handover target selection
4. Handover Execution → Switch to target satellite
Measurement-Based Challenges in LEO:
- Doppler Shift: Rapid frequency changes affect measurements
- Measurement Delays: 150-300ms propagation delays
- Small Signal Difference: Similar RSRP between cell center and edge
Method | Description | Advantages | Disadvantages
RSS/RSRP-based | Select strongest signal | Simple, 3GPP standard | Frequent handovers, ping-pong
Elevation Angle | Highest elevation priority | Better link quality, lower path loss | May not optimize service time
Service Time | Maximize visibility duration | Reduces HO frequency, predictable | May sacrifice signal quality
Multi-Criteria (MADM) | Weighted combination using AHP/TOPSIS | Balanced approach, customizable | Static optimization, complexity

## Slide 5: Measurement Report-based Handover (AI-Enhanced Approaches)
Deep Reinforcement Learning Methods:
Deep Q-Network (DQN) Based
State: [RSRP, elevation angle, visible time, load, interference]
Action: Target satellite selection from coverage set
Reward: Throughput - handover penalty - outage cost
Innovation: Learns optimal measurement thresholds dynamically
Performance: 30-50% reduction in handover rate
Multi-Agent Deep Q-Network (MADQN)
Architecture: Distributed learning, each UE as independent agent
Coordination: Implicit through environment interaction
State Space: Local information only (scalable)
Benefits: 95% handover reduction, real-time adaptation
Paper Reference: Lee et al. (2025) - simultaneous decision making

## Slide 6: Measurement Report-based Handover (AI-Enhanced Approaches)
Multi-Objective Reinforcement Learning (MORL)
Objectives: Maximize [throughput, QoS] + Minimize [handovers, energy]
Method: Pareto-optimal solution selection
Algorithm: MODQN (Multi-Objective DQN)
Application: Multi-beam LEO satellites
Achievement: 62% throughput improvement
Game Theory + RL (Nash-SAC)
Approach: Nash equilibrium in multi-user scenarios
Users: Aircraft, drones, ground terminals
Algorithm: Soft Actor-Critic with Nash solutions
Performance: 16% handover reduction, 48% utility improvement
Advantage: Handles heterogeneous user requirements

## Slide 7: Non-Measurement Report-based Handover (Traditional)
Approaches Without Measurement Reports:
Location-based Handover
3GPP D2 Event: Uses UE position and satellite ephemeris from SIB19
Trigger Condition: Distance calculations based on GPS coordinates
Advantages: Zero measurement delays, predictable, eliminates RLF
Implementation: Real-time distance monitoring with hysteresis
Time-based Handover
Mechanism: Pre-scheduled switching using Two-Line Element (TLE) data
Method: Timer-based handover at predetermined orbital positions
Advantages: Completely deterministic, no measurement overhead
Limitation: Cannot adapt to dynamic channel conditions or interference

## Slide 8: Non-Measurement Report-based Handover (Traditional)
Approaches Without Measurement Reports:
Conditional Handover (CHO)
3GPP Rel-16: Enhanced mobility for Non-Terrestrial Networks (NTN)
Pre-configuration: Target satellite parameters configured in advance
Execution Triggers: Time-based, location-based, or hybrid conditions
Benefits: 84% reduction in signaling overhead, improved reliability
Graph-based Methods
Network Flow: Time-expanded graphs with satellites as nodes
Algorithms: Shortest path, minimum cost flow, maximum flow solutions
Optimization: Global handover path planning considering future states
Complexity: O(N³T) for N satellites and T time slots

## Slide 9: Non-Measurement Report-based Handover (AI-Enhanced)
AI-Enhanced Predictive Methods:
Predictive Deep RL
Orbital Prediction: Skip measurement reports using Keplerian orbital mechanics
Training Data: Historical satellite positions, channel conditions, user mobility
Neural Architecture: LSTM + DQN for temporal sequence learning
Benefits: 150-300ms latency reduction, proactive handover decisions
Graph Neural Networks (GNN)
Dynamic Topology: Learn optimal paths in time-varying satellite constellation
Node Features: Satellite position, load, beam coverage, interference level
Edge Weights: Inter-satellite distances, link quality, handover costs
Performance: Distributed decision making with global optimization

## Slide 10: Non-Measurement Report-based Handover (AI-Enhanced)
Transformer-based Channel Prediction
Attention Mechanism: Learn long-term channel dependencies
Input Sequence: Historical RSRP, satellite positions, Doppler shifts
Prediction Horizon: 10-30 seconds ahead for proactive handover
Accuracy: 95% correlation with actual measurements
Joint Optimization with Model Predictive Control (MPC)
Multi-Objective: Handover decisions + resource allocation + power control
Prediction Model: Satellite constellation dynamics and user mobility
Optimization Horizon: 60-120 seconds rolling window
Results: 62% throughput improvement, 40% energy savings
Advanced AI Features:
Digital Twin Networks: Real-time network state mirroring
Federated Learning: Privacy-preserving distributed training
Meta-Learning: Fast adaptation to new satellite constellations

## Slide 11: Performance Comparison Analysis
Quantitative Performance Metrics:
Metric | Traditional Methods | AI-Enhanced Methods | Best Performing Approach
Handover Rate | 0.8-1.2 HO/min | 0.05-0.2 HO/min (85% ↓) | MADQN + Location-based
Radio Link Failures | 15-40% | <1% | CHO + Predictive RL
Average Throughput | 12-18 Mbps | 20-29 Mbps (62% ↑) | Joint Optimization MPC
End-to-End Latency | 180-320 ms | 90-160 ms (50% ↓) | Non-measurement + GNN
Signaling Overhead | 450-680 msgs/min | 70-120 msgs/min (84% ↓) | Distributed MARL
QoS Satisfaction Time | 65-80% | 92-98% | Nash-SAC multi-objective
Energy Efficiency | 2.1-2.8 bits/Joule | 3.4-4.2 bits/Joule (85% ↑) | Energy-aware DRL

## Slide 12: Performance Comparison Analysis
Performance vs. Complexity Trade-offs:
N = number of satellites, T = time horizon, M = state space size, K = number of users
Approach Category | Computational Complexity | Implementation Difficulty | Real-time Capability | Performance Gain
Traditional Rule-based | O(N) | Low | Excellent | Baseline
3GPP Events (D2, A4, A5) | O(N log N) | Medium | Very Good | 20-30%
Graph-based Optimization | O(N³T) | High | Poor | 35-45%
Single-agent RL (DQN) | O(MN) | Medium-High | Good | 50-65%
Multi-agent RL (MADQN) | O(KMN) | High | Very Good | 70-95%